## Slide 1: 8086 Assembler Directives

## Slide 2: ASSEMBLER DIRECTIVES
Assembler directives are the commands to the assembler that direct the assembly process.
They indicate how an operand is treated by the assembler and how assembler handles the program.
They also direct the assembler how program and data should arrange in the memory.
ALP’s are composed of two type of statements.
The instructions which are translated to machine codes by assembler.
The directives that direct the assembler during assembly process, for which no machine code is generated.

## Slide 3: Important Assembler Directives of the 8086 Microprocessor
Data declaration directives: DB, DW, DD, DQ, DT
ASSUME
END directives
EQU Directive
PROC
ORG
SEGMENT
GROUP, INCLUDE, EVEN, ALIGN
EXTRN, PUBLIC,
TYPE, PTR,
LENGTH, OFFSET
NAME, LABEL, SHORT, GLOBAL

## Slide 4
1. ASSUME: Assume logical segment name
Syntax:
ASSUME segreg:segname,…segreg:segname
Ex:
ASSUME CS:CODE
ASSUME CS:CODE,DS:DATA,SS:STACK

## Slide 5
2. DB: Define Byte
The DB directive is used to reserve byte or bytes of memory locations in the available memory.
Syntax:
Name of variable DB initialization value.
Ex: MARKS DB 35H,30H,35H,40H
NAME DB “VARDHAMAN

## Slide 6
3. DW: Define Word
The DW directive serves the same purposes as the DB directive, but it now makes the assembler reserve the number of memory words(16-bit) instead of bytes.
Syntax:
variable name DW initialization values.
Ex: WORDS DW 1234H,4567H,2367H
WDATA DW 5 Dup(522h)
(or) Dup(?)

## Slide 7
4. DD: Define Double:
The directive DD is used to define a double word (4bytes) variable.
Syntax:
variable name DD 12345678H
Ex: Data1 DD 12345678H

## Slide 8
5. DQ: Define Quad Word
This directive is used to direct the assembler to reserve 4 words (8 bytes) of memory for the specified variable and may initialize it with the specified values.
Syntax:
Name of variable DQ initialize values.
Ex: Data1 DQ 123456789ABCDEF2H

## Slide 9
6. DT: Define Ten Bytes
The DT directive directs the assembler to define the specified variable requiring 10 bytes for its storage and initialize the 10-bytes with the specified values.
Syntax:
Name of variable DT initialize values.
Ex: Data1 DT 123456789ABCDEF34567H

## Slide 10
7. END: End of Program
The END directive marks the end of an ALP. The statement after the directive END will be ignored by the assembler.

## Slide 11
8. ENDP: End of Procedure
The ENDP directive is used to indicate the end of procedure. In the AL programming the subroutines are called procedures.
Ex:
Procedure Start
:
Start ENDP

## Slide 12
9. ENDS: End of segment
The ENDS directive is used to indicate the end of segment.
Ex:
DATA SEGMENT
:
DATA ENDS

## Slide 13
10. EVEN: Align on Even memory address
The EVEN directives updates the location counter to the next even address.
Ex: EVEN
Procedure Start
:
Start ENDP
  The above structure shows a procedure START that is to be aligned at an even address.

## Slide 14
11. EQU: Equate
The directive EQU is used to assign a label with a value or symbol.
Ex: LABEL EQU 0500H
ADDITION EQU ADD

## Slide 15
EXTRN: External and public
The directive EXTRN informs the assembler that the names, procedures and labels declared after this directive have been already defined in some other AL modules.
While in other module, where names, procedures and labels actually appear, they must be declared public using the PUBLIC directive.
Ex: MODULE1 SEGMENT PUBLIC FACT FAR
MODULE1 ENDS
MODULE2 SEGMENT EXTRN FACT FAR
MODULE2 END

## Slide 16
13. GROUP: Group the related segments
This directive is used to form logical groups of segments with similar purpose or type. Ex: PROGRAM GROUP CODE, DATA, STACK*CODE, DATA and STACK segments lie within a 64KB memory segment that is named as PROGRAM.

## Slide 17
14. LABEL: label
The label is used to assign name to the current content of the location counter.
Ex: CONTINUE LABEL FAR
The label CONTINUE can be used for a FAR jump, if the program contains the above statement.

## Slide 18
15. LENGTH: Byte length of a label
This is used to refer to the length of a data array or a string.
Ex : MOV CX, LENGTH ARRAY

## Slide 19
LOCAL:
The labels, variables, constant or procedures are declared LOCAL in a module are to be used only by the particular module.
Ex : LOCAL a, b, Data1, Array, Routine

## Slide 20
17. NAME: logical name of a module
The name directive is used to assign a name to an assembly language program module. The module may now be refer to by its declared name.
Ex : Name “addition”

## Slide 21
18. OFFSET: offset of a label
When the assembler comes across the OFFSET operator along with a label, it first computing the 16-bit offset address of a particular label and replace the string ‘OFFSET LABEL’ by the computed offset address.
Ex : MOV SI, offset list

## Slide 22
19. ORG: origin
The ORG directive directs the assembler to start the memory allotment for the particular segment, block or code from the declared address in the ORG statement.
Ex: ORG 1000H

## Slide 23
20. PROC: Procedure
The PROC directive marks the start of a named procedure in the statement.
Ex: RESULT PROC NEAR
ROUTINE PROC FAR

## Slide 24
21. PTR: pointer
The PTR operator is used to declare the type of a label, variable or memory operator.
Ex : MOV AL, BYTE PTR [SI]
MOV BX, WORD PTR [2000H]

## Slide 25
22. SEG: segment of a label
The SEG operator is used to decide the segment address of the label, variable or procedure.
Ex : MOV AX, SEG ARRAY
MOV DS, AX

## Slide 26
23. SEGMENT: logical segment The segment directive marks the starting of a logical segment
Ex: CODE SEGMENT: CODE ENDS
24.SHORT: The SHORT operator indicates to the assembler that only one byte is required to code the displacement for jump.
Ex : JMP SHORT LABEL

## Slide 27
25. TYPE:
The TYPE operator directs the assembler to decide the data type of the specified label and replaces the TYPE label by the decided data type.
For word variable, the data type is 2.
For double word variable, the data type is 4. For byte variable, the data type is 1.
Ex : STRING DW 2345H, 4567H
MOV AX, TYPE STRING AX=0002H

## Slide 28
26. GLOBAL: The labels, variables, constants or procedures declared GLOBAL may be used by other modules of the program.
Ex : ROUTINE PROC GLOBAL.
27. FAR PTR: This directive indicates the assembler that the label following FAR PTR is not available within the same segment and the address of the label is of 32-bits i.e 2-bytes of offset followed by 2-bytes of segment address.
Ex : JMP FAR PTR LABEL

## Slide 29
28. NEAR PTR:
This directive indicates that the label following NEAR PTR is in the same segment and needs only 16-bit i.e 2-byte offset to address it.
Ex : JMP NEAR PTR LABEL
CALL NEAR PTR ROUTINE

## Slide 30
8086 Programming using Assembler Directives:1st form
Basic structure of a program:
.DATA
Data declaration statement 1
:
:
Data declaration statement n
.CODE
MAIN PROC
Program line 1
:
:
Program line n
END MAIN

## Slide 31: Example-2
Program to multiply 2 16-bit words in memory locations called MULTIPLICAND and MULTIPLIER. Result is stored in memory location PRODUCT.
.DATA
MULTIPLICAND DW 204A H ; 1ST Word
MULTIPLIER DW 3B2A H ; 2nd word
PRODUCT DW 2 DUP(0) ; sets aside storage for 2 words in memory and gives starting address
; of 1st word the name PRODUCT. The DUP(0) part of the statement
;tells assembler to initialize 2 words to all zeros.
.CODE
MAIN PROC
MOV AX, DATA MOV DS, AX
MOV AX, MULTIPLICAND
MUL MULTIPLIER
MOV PRODUCT, AX
MOV PRODUCT+2, DX
INT3 ; OPTIONAL. CAN
; BE USED OTHER
; TYPE OF
; INTERRUPT TO
; EXIT FROM THE ; PROGRAM
END MAIN

## Slide 32: 8086 Programming using Assembler Directives: 2nd form
Basic structure of a program:
Name_data segment SEGMENT
Data declaration statement 1
:
:
Data declaration statement n
DATA ENDS
Name_codeseg SEGMENT
ASSUME CS:CODE, DS:DATA, ES:EXTRA, SS: STACK START:
Program line 1
:
:
Program line n
Name_codeseg ENDS END START

## Slide 33: Example-2
Program to multiply 2 16-bit words in memory locations called MULTIPLICAND and
MULTIPLIER. Result is stored in memory location PRODUCT.
DATA SEGMENT
MULTIPLICAND DW 204A H ; 1ST Word MULTIPLIER DW 3B2A H ; 2nd word
PRODUCT DW 2 DUP(0) ; sets aside storage for 2 words in memory and gives starting address of
;1st word the name PRODUCT. The DUP(0) part of the statement tells
; assembler to initialize 2 words to all zeros.
DATA ENDS
CODE SEGMENT
ASSUMER CS:CODE, DS:DATA;
START:
MOV AX, DATA MOV DS, AX
MOV AX, MULTIPLICAND
MUL MULTIPLIER
MOV PRODUCT, AX
MOV PRODUCT+2, DX
INT 3 ; OPTIONAL. CAN BE USED
; OTHER TYPE OF INTERRUPT TO
; EXIT FROM THE PROGRAM
CODE ENDS
END START

## Slide 34
OBJECTIVE:
Find the largest and smallest number in a given array of size N.
Arrange the elements of a given array of size N in ascending and descending order.

## Slide 35
OBJECTIVE:
Find the largest number in a given array of size N.
PROGRAM:
.data
count db 04h ; count = array size
value db 09h, 10h,05h,03h ; array elements
res db 0 ; store the result in res

## Slide 36
.code
MAIN PROC
mov ax, data
mov ds, ax
mov cl, count
dec cl
LEA SI, value
mov al, [SI]
up: inc si
cmp al, [si]
jnl nxt
mov al, [si]
nxt: dec cl
jnz up
LEA DI, res
mov [DI], al
END MAIN

## Slide 37
OBJECTIVE:
Arrange the elements of an given array of size N in ascending order.
PROGRAM:
.DATA
count DB 06
value DB 09H,0FH,14H,45H,24H,3FH
.CODE
MAIN PROC
MOV AX,DATA
MOV DS,AX
MOV CH, count
DEC CH

## Slide 38
UP2: MOV CL,CH
LEA SI, value
UP1: MOV AL,[SI]
CMP AL,[si+1]
JC DOWN
MOV DL,[SI+1]
XCHG [SI],DL
MOV [SI+1],DL
DOWN: INC SI
DEC CL
JNZ UP1
DEC CH
JNZ UP2
END MAIN